## Slide 1: EEG Paradigms
Course Instructor
Dr. Annushree Bablani
Acknowledgments: Dr Sreeja SR

## Slide 2: Direct (noninvasive) interfaces in EEG
An event-related potential (ERP) is any measured brain response that is directly the result of a thought or perception. More formally, it is any stereotyped electrophysiological response to an internal or external stimulus.
Direct Interfaces via EEG
  VEP – Visual Evoked Potential
  AEP – Auditory Evoked Potential
  SSVEP – Steady-State Visual Evoked Potential
  P300 – ERP elicited by infrequent, task-relevant stimuli.
  ERS/ERD – Event related synchronization/desynchronization
  SCP – Slow cortical potentials

## Slide 3: Categorization of EEG based BCI paradigms
Evoked (Endogenous / Asynchronous)
Subject must pay attention for a certain time to external cues (e.g. flashes, sounds, etc.)
Cue-based
Spontaneous (Exogenous / Synchronous)
No continuous attention to specific stimulus is necessary
User-driven

## Slide 4: Categorization of EEG based BCI paradigms
ERD | Spontaneous
P300 | Evoked
SSEP/AEP/VEP | Evoked
SCP | Spontaneous

## Slide 5: Event Related Potentials (ERP)
Averaging of trials following a stimulus

## Slide 6: Visual Evoked Potential (VEP)
Caused by Visual Stimulus
Occurs with flashing lights (3-5 Hz)
Have been used to monitor function during surgery for lesions involving the pituitary gland, optic nerve.
Application:

## Slide 7: Steady-State Visual Evoked Potential (SSVEP)
SSVEP are signals that are natural responses to visual stimulation at specific frequencies. When the retina is excited by a visual stimulus ranging from 3.5 Hz to 75 Hz, the brain generates electrical activity at the same (or multiples of) frequency of the visual stimulus.
Excellent signal-to-noise ratio and relative immunity to artifacts.
Applications:
  SSVEP-controlled robots (Boston University)
  User-friendly interface

## Slide 8: P300
P300 is thought to reflect processes involved in stimulus evaluation or categorization.
It is usually elicited using the oddball paradigm in which low-probability target items are inter-mixed with high-probability non-target (or "standard") items.
Results in a positive curve on EEG after 300ms.
Strongest signal at parental lobe.
6x6 matrix of symbols
Subject concentrates on a symbol (i.e. cell)
Each row and column flashes twice
  i.e. 2 target flashes vs. 10 non-target flashes
  random order
  for very short time (e.g. 100 ms)

## Slide 9: P300
(Farwell and Donchin 1988)
95% accuracy at 1 character per 26s

## Slide 10: ERS/ERD
Event-related desynchronization (ERD) and event-related synchronization (ERS) is the change of signal's power occurring in a given band, relative to a reference interval.
People have naturally occurring brain rhythms over areas of the brain concerned with touch and movement. When people imagine moving, these brain rhythms first become weaker, then stronger. These two changes are called ERD and ERS, respectively.
ERS
  oscillatory power increase
  associated with activity decrease
ERD
  oscillatory power decrease
  associated with activity increase

## Slide 11: ERS/ERD
The imagination of either a left or right hand movement results in:
  An amplitude attenuation (Event-Related Desynchronization (ERD)) of μ (8-12Hz) and central beta EEG-rhythms (13-30Hz) at the contralateral sensorial motor representation area and,
  in some cases, in an amplitude increase (Event-Related Synchronization (ERS)) within the γ-band (30-40Hz) at the ipsi-lateral hemisphere(6).
EEG recorded from C3 electrode.

## Slide 12: ERS/ERD (4)
Post-Stimulus
Pre-Stimulus
Stimulus
Post-Stimulus
Pre-Stimulus
Time
Theta
Amplitude
Time
Alpha
Amplitude
ERS
ERD
Stimulus
Typical Theta response
Apha response

## Slide 13: Communication Issues
Typical training time versus communication bitrate for the three main types of noninvasive EEG based BCIs.

## Slide 14: BCI Applications
  BCI – operated robot

## Slide 15: BCI Applications

## Slide 16: BCI Applications

## Slide 17: BCI Applications

## Slide 18: Thank you!